## Slide 1: System Design Lane simulation

## Slide 2
Table of contents
  Panel design
  Panel design and data flow
  Concept
  Curvature (arc)
  Curvature calculation (for point-based representation; arc)
  Curvature calculation (for point-based representation; clothoid)
  Lane departure simulation (TBD)
  Road scenarios (TBD)

## Slide 3
Panel design

## Slide 4
Panel design and data flow
Lane Panel
Lane segment
Segment/Line ID
Lane width
Road edge offset
Raised edge offset
Line type
Activaton (using switches) of segments (L, R, LL, RR, etc.)
Vehicle motion
Heading direction (Left, Right)
Heading angle (deg)
Wheel activation duration
Road secnarios
list of pre-defined road scenarios:
  straight (default)
  curve 1 (simple curvature without curvature change, r1)
  curve 2 (simple curvature without curvature change, r2)
  curve 3 (curvature with curvature change)
Length of road (read only)
Position on road (read only)
CLOE :: Lines
- via FDX protocol
- simulation source: video
Internal data structure to store simulated Lane segments
(max 8 segments)
- Segment/Line ID [1 .. 8]
- Line type
- Line Relation (right, left, etc…)
- Line Distance y
- Line Curvature (1/m)
- Line Curvature Change (1/m*m)
- Line Distance x Start
- Line Distance x End
User
Vehicle Model data structure
Customer / Bosch COM protocols
Representation =
Curvature-based
OR Point-based

## Slide 5
Concept
Heading angle
Heading angle
Road curvature
Lane width
Line Left
Line Right
NOTE:
Curvature of Line segments is derived from Road curvature
Line position (Dy) is calculated from Vehicle Head position (based on Lane width)
Dy

## Slide 6
Curvature (arc)
R
R
R
α
α = 1 rad
1 rad (in degree) | 57,29577951 |  |  | 
radian (rad) | 1 | 1 | 1 | 1
radius (m) | 1 | 500 | 100 | 100000
curv (rad/m) | 1 | 0,002 | 0,01 | 0,00001
rad to degree | 57,29577951 | 0,114591559 | 0,572958 | 0,000573
Example in ADASIS v2 protocol description

## Slide 7
Curvature calculation (for point-based representation; arc)
R
Where:
β = (α / resolution) / 2
a = 2 * R * sinβ
tan : tangent at joints
β
β
β
R
tan
tan
90°
a
a
a
P1
P2
Point calculation:
P1 (x1, y1)
y1 = sinβ * a
x1 = cosβ * a
P2 (x2, y2)
y2 = sin(2*β) * a + y1
x2 = cos(2*β) * a + x1
P2 (x3, y3)
y3 = sin(3*β) * a + y2
x3 = cos(3*β) * a + x2
tan
R
α
α
P3

## Slide 8
Curvature calculation (for point-based representation; clothoid)
R1
Where:
β = (α / resolution) / 2
γ = curvature change / resolution
tan : tangent at joints
β + γ
β + γ
β
R2
tan
tan
90°
a
a
a
P1
P2
Point calculation:
TBD
β + γ
R0
TBD

## Slide 9
Lane departure simulation
Heading angle
Road curvature
Lane width
Line Left
Line Right
NOTE:
DyMin is the distance the vehicle needs to move back towards lane center
The vehicle shall follow the lane direction after returning the center of the lane
In case of straight road scenarios, lane departure has to be started by user
In case of curvature road scenarios, the vehicle shall adapt automatically to the road conditions (no additional lane departure activation is needed by the user)
Dy < DyMin

## Slide 10
Distance to lane border
DistToRightBorder
DistToLeftBorder
VehWidth
VehLength
DyLeft
DyRight
α
α
TBD

## Slide 11
Road scenarios
Straight Road:
  This road scenario is iterative, simulated continuously
Curvature (arc):
  This road scenario is simulated only once. When the vehicle passed this road section, Straight Road is started to simulate