## Slide 1: System Design Multipurpose radar model

## Slide 2
Multipurpose Radar model - Concept
Concept: The main concept of Multipurpose Radar model to simulate radar objects/locations from the same radar sensor for both Driving and Parking applying alternation of the simulated content.
Solution:
    Simulation environment (the radar content is received from): CaRMaker
    RBS environment (bus communation): CANoe
    The simulated objects/location are received from CarMaker
    CANoe should be able to request the source, which could be either Driving or Parking sensor
    Same object/location data structure should be used for both Driving and Parking contents (to keep used CANoe-CarMaker API load as lower as possible)
Implementation:
  Sensor set:
    Two sensor based concept (on CarMaker side, there are dedicated radar sensors configured for Driving and Parking contents)
    One sensor base concept (on CarMaker side, there is one radar sensor configured for Driving and Parking content)
  Dataflow

## Slide 3
Multipurpose Radar model - Two sensor based concept
CarMaker
radar type request
CANoe
APO
detected radar object(s)
RB interface
Radar RCS + Object sensors
Driving
Parking
if Radar type == Driving then
send Driving obj
else
send Parking obj
RoadObj sim
Bus
msg Tx
Data flow:
detected radar object(s) and sender type depend on Radar type (Driving or Parking)
Radar type is changed/requested by CANoe
  if Variant is Driving only then Radar type is Driving
  if Variant is Parking only then Radar type is Parking
  if Variant is D&P then Radar type is alternating in every 50ms (typically at msg Tx on bus) between D and P NOTE: it is important to let CANoe to decide, which object is actually needed from CM. Othwewise CM would be the „master” regarding which type of object to send on Bus.
Object sent on Bus (msg Tx) depends on received sender type
sender type

## Slide 4
Multipurpose Radar model - One sensor based concept
Data flow:
Same as two sensor based concept
CarMaker
radar type request
CANoe
APO
detected radar object(s)
RB interface
Radar RCS + Object sensor
(multi purpose radars - P&D)
if Radar type == Driving then
  change sensor parameters to
  send Driving obj
else
  change sensor parameters to
  send Parking obj
RoadObj sim
Bus
msg Tx
Radar objects
sender type

## Slide 5
Multipurpose Radar model - Dataflow
radar_type_req
Bus (objects)
50ms
50ms
50ms
50ms
50ms
50ms
Parking
Driving
Parking
Driving
CarMaker radar content
Init
Parking
Driving
Parking
Driving
Parking
Driving